LM9830 Setup for Dyna Image DL408-03CSM

| LM9830 Reg # (hex) | LM9830 Register Name | Data Value Hex (decimal) | Purpose |
| --- | --- | --- | --- |
| 08 | MCLK Divider | 0A (10) | MCLK = 8 MHz, pixel rate = 1MHz |
| 09 | HRES/Datamode | 18 (24) | 8 bits/pixel, 8 bit data, full pixel rate (/1) |
| 0A | Reserved | 00 (0) | Must be 0 in LM9830 |
| 0B | Sensor Config | 09 (9) | Positive polarity (CIS), CDS off, Standard sensor, 600dpi (supports > 2731 pixels) |
| 0C | Polarity | 00 (0) | All signals positive polarity |
| 0D | Active/Off | 24 (36) | Only TR1 and RST required |
| 0E | TR Guardband | 00 (0) | Not used in this mode |
| 0F | Clamp start | 01 (1) | Sets start of internal clamp |
| 10 | Clamp end | 06 (6) | Sets end of internal clamp |
| 11 | Reset Pulse Start | 07 (7) | Sets Reset Pulse Timing |
| 12 | Reset Pulse End | 00 (0) | “ “ “ “ |
| 13 | CP1 Pulse Start | 07 (7) | Sets CP1 Pulse Timing |
| 14 | CP1 Pulse End | 00 (0) | “ “ “ “ |
| 15 | CP2 Pulse Start | 07 (7) | Sets CP2 Pulse Timing |
| 16 | CP2 Pulse End | 00 (0) | “ “ “ “ |
| 17 | Reference Position | 06 (6) | (Ignored, not using CDS) |
| 18 | Signal Sample posn. | 06 (6) | Sets signal sample timing |
| 19 | CIS Timing | 05 (5) | CIS Mode 1, Fake optical black pixels on (specific to Dyna CIS modules) |
| 1A | Reserved | 00 (0) | Must be 0 in LM9830 |
| 1B | Reserved | 00 (0) | Must be 0 in LM9830 |
| 1C | Optical black start | 00 (0) | 32 “fake” black pixel for… |
| 1D | Optical black end | 1F (31) | …DC-restoring clamp |
| 1E | Active Pix Start MSB | 00 (0) | First active pixel |
| 1F | Active Pix Start LSB | 20 (32) | is 32nd pixel |
| 20 | Line end MSB | 0E (14) | One scanline = 3700 pixels |
| 21 | Line end LSB | 74 (116) | (leaves room for adjustment) |
| 22 | Data pix start MSB | 00 (0) | First data pixel is |
| 23 | Data pix start LSB | 20 (32) | Pixel number 32 |
| 24 | Data pix end MSB | 0E (14) | Last data pixel is |
| 25 | Data pix end LSB | 5F (95) | Pixel number 3679 |
| 26 | Color Mode | 14 (20) 10 (16) | 1 CIS module: 1 channel Mode A color using blue channel 2 or 3 CIS modules: 3 channel pixel rate color |
| 27 | Integration Time adj | 00 | Not used in this mode |
| 28 | Reserved | 00 | Must be 0 in LM9830 |
| 29 | Illum. Mode | 01 | PWM Mode |
| 30 | Glamp (PWM) MSB | 00 08 0F | PWM MSB value Illum. Off Illum. 50% Illum. 100% |

| LM9830 Reg # (hex) | LM9830 Register Name | Data Value Hex (decimal) | Purpose |
| --- | --- | --- | --- |
| 31 | Glamp (PWM) LSB | 00 00 FF | PWM LSB value Illum. Off Illum. 50% Illum. 100% |
| 2C-37 | RGB Illum on/off | 00 | Not used, write 00 |
| 38-3D | RGB gain/offset (static) | 00 | Determined by calibration Use 00 temporarily |
| 3E | Gain | 07 | Bypasses RAM coefficients |
| 3F-41 | Add’l gain/offset | 00 | Determined by calibration |
| 42 | Port Mode | 06 | EPP Mode, Max drive (14ma) **MUST BE FIRST REGISTER WRITTEN INTO** |
| 43 | SRAM Config | 1E | 256K, 5ns, slot mode, Full duplex |

NOTES:

1) 	Calibration process determines values for registers 38-41.  Register 3E is set to 07 to bypass the SRAM coefficients, using only the static offsets in the configuration registers during coarse calibration.  After coarse calibration, Register 3E is set as required by the calibration process.

2)	If a stepper motor has NOT been properly configured, remove all jumpers from JP1 and set register 45 (hex) to 00 to disable and protect the stepper drivers.