Instructions for Connecting Dyna Image DL408-03CSM CIS Modules to the RollSCAN-1 Scanner Controller Board

The following instructions assume that you are using 1, 2 or 3 Dyna Image DL408-03CSM modules with CCFL illumination using JKL Lamps BXA-12579/INV inverters:

- Use the CCFL on the sensor for frontlight or a separate 360mm CCFL (JKL Lamps P/N BF3360-20B for backlight.

- Install a jumper across JP4 pins 1 and 2 (connects DGND to AGND).

- Connect a stable 15V power supply to RollSCAN-1 J5 pin 3 (Illuminator power)

- Connect a stable 5V supply to RollSCAN-1 J5 pin 2 (CCD/CIS power).

- Don't forget to connect the power supply negative (ground) terminals to RollSCAN-1 J5 pins 5 and 6.

- It is OK to use the 15V supply for bulk logic power as well (RollSCAN-1 J5 pin 1).

- Install jumpers across JP5, JP6, and JP7 pins 1-2

Make your CIS and inverter connections according to the following table:

| RollSCAN-1 J6 Pin # | Signal Name | CIS 1 Pin # | CIS 2 Pin # | CIS 3 Pin # | Inverter Input Pin # |
| --- | --- | --- | --- | --- | --- |
| 1,2 | VD | -- | -- | -- | -- |
| 3,4,12 | PGND | -- | -- | -- | 5,6 |
| 5,6 | VCCD | 1 | 1 | 1 |  |
| 7,8 | VI | -- | -- | -- | 1,2 (Note 1) |
| 9 | LEDR | -- | -- | -- | -- |
| 10 | LEDG | -- | -- | -- | 3 (Note 2) |
| 11 | LEDB | -- | -- | -- | -- |
| 13 | VREF | -- | -- | -- | -- |
| 14,18,26 | GND | (Note 3) | (Note 3) | (Note 3) | -- |
| 15 | OS_R | -- | -- | 5 | -- |
| 16 | OS_G | -- | 5 | -- | -- |
| 17 | OS_B | 5 | -- | -- | -- |
| 19 | CP1 | -- | -- | -- | -- |
| 20 | CP2 | -- | -- | -- | -- |
| 21 | TR1 | 10 | 10 | 10 | -- |
| 22 | TR2 | -- | -- | -- | -- |
| 23 | CLK1 | -- | -- | -- | -- |
| 24 | CLK2 | -- | -- | -- | -- |
| 25 | RST | 12 | 12 | 12 | -- |

(-- = No connection)

NOTES:

Note 1:	Although the JKL inverter spec lists the power supply as 12 Volts, parasitic capacitances due to the routing of the CCFL wiring load down the output, necessitating a higher output.  The JKL tech support department has said that the 15V supply is OK.

Note 2:	This connection is for CCFL illumination only, assuming PWM (pulse width modulation) control of the CCFL intensity. Connect a 4.7K pullup resistor from inverter input pin #3 to inverter input pin #2.

Note 3:	Dyna CIS has multiple ground connections.  Connect RollSCAN-1 J6 pins 14, 18 and 26 to all CIS modules, pins 2,4,6,7,9 and 11.